## Slide 1
Design & Verification of an
8-bit RISC-V Inspired Processor
Single-Cycle Architecture • 2-Stage Pipeline with Data Forwarding • Verilog HDL in Xilinx Vivado
Internship Guide: [Mentor Name]
Duration: [Start] – [End], 2026
01
Submitted by : Vaibhav Shromani
Branch: Electronics & Communication Engineering
Institute: Maulana Azad National Institute Of Technology
Internship: VLSI Design- Technnglobal Industial Training Program
Github Repository: https://github.com/vaibhavshromani/8_bit_RISC_V
DESIGN • VLSI • VERILOG HDL

## Slide 2
ROADMAP
Agenda
01
Objective
02
Instruction Set Architecture
03
Datapath Architecture
04
Module-Level Verilog Design
05
Simulation & Verification
06
Pipelining & Hazards
07
Synthesis in Vivado
08
Learnings & Conclusion
02
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 3
WHY THIS PROJECT
Project Overview & Objective
What is a RISC Processor?
A Reduced Instruction Set Computer (RISC) processor executes simple, fixed-length instructions in a single clock cycle using a load-store architecture. This project implements a 8-bit 2-stage pipelined RISC processor in Verilog HDL — integrating datapath, control logic, pipelined register, register file, ALU, instruction memory, and data memory into a fully simulated and synthesized digital system..
03
Design a 8-bit 2-stage pipelined RISC processor (Fetch + Execute/Writeback) in Verilog HDL.
Implement 6 instructions: ADD, SUB, AND, OR, LOAD, STORE with a 4-bit opcode ISA.
Build modular sub-components: PC, Instruction Memory, Control Unit, Register File, ALU, Data Memory Verify
correctness via comprehensive testbench with pass/fail assertions on register and RAM state.
Synthesize and implement on FPGA using Xilinx Vivado; generate RTL schematic and power/timing reports
Document all design decisions, ISA, datapath, and results as required by mentor checklist
Project Objective

## Slide 4
Parameter | Value
Architecture | Custom RISC
Data Width | 8-bit
Instruction Width | 16-bit
Registers | 8 Registers (R0-R7)
Register Width | 8-bit
Instruction Memory | 16 × 16-bit
Data Memory | 32 × 8-bit
Pipeline | 2-Stage
Clocking | Single Clock
HDL | Verilog
Tool Used | Xilinx Vivado
Processor Specifications

## Slide 5
INSTRUCTION SET ARCHITECTURE (ISA)
8-bit Datapath, 16-bit Instruction Word
Custom ISA — 6 instructions across 2 formats
Opcode | Mnemonic | Format | Operation
000 | ADD | R-type | rd = rs1 + rs2
001 | SUB | R-type | rd = rs1 − rs2
010 | AND | R-type | rd = rs1 & rs2
011 | OR | R-type | rd = rs1 ¦ rs2
100 | LOAD | I-type | rd = Mem[base + imm]
101 | STORE | I-type | Mem[base + imm] = rd
R0 is hardwired to zero (standard RISC convention).
R-TYPE (16 bits)
opcode[3] | rd[3] | rs1[3] | rs2[3] | unused[4]
e.g. ADD R3, R1, R2
I-TYPE (16 bits)
opcode[3] | reg[3] | base[3] | imm[7]
e.g. LOAD R1, 0x10
8 × 8-bit registers • 32 × 8-bit data RAM • 16 × 16-bit instruction ROM
04
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 6
ARCHITECTURE
Single-Cycle Datapath
PC
4-bit
Instruction
Memory
16×16-bit
Register
File
8×8-bit
ALU
ADD/SUB/AND/OR
Data
Memory
32×8-bit
Write-Back
Mux
to Reg File
Control Unit
decodes opcode → reg_write, mem_write, mem_read, alu_src, mem_to_reg, alu_op
write_back_data
Fetch (PC→IMEM) → Decode (opcode→Control Unit, operands→Register File) → Execute (ALU) → Memory Access (LOAD/STORE) → Write-Back — all completing within one clock cycle.
05
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 7
RTL STRUCTURE
Module-Level Breakdown
pc.v
Program Counter
4-bit counter; increments each clock, resets to 0, saturates at 15.
instruction_memory.v
Instruction ROM
16 × 16-bit words, preloaded with the sample program, word-addressed by PC.
control_unit.v
Control Unit
Combinational decoder: opcode → 5 control signals + 2-bit alu_op.
register_file.v
Register File
8 × 8-bit regs, 2 combinational read ports, 1 synchronous write port. R0 = 0.
alu.v
ALU
9-bit internal adder catches carry-out; supports ADD / SUB / AND / OR.
data_memory.v
Data Memory
32 × 8-bit RAM, combinational read + synchronous write, preloaded test data.
06
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 8
RTL Schematic - Xilinix Vivado

## Slide 9
RTL CODE SPOTLIGHT
alu.v — Combinational Logic Core
Design notes
9-bit internal `temp` register — the extra MSB captures carry-out from ADD without any separate adder hardware.
Reuses the same combinational case-statement style as the earlier 8-bit ALU minor project, trimmed to the 4 ops this ISA needs.
`zero` flag is derived combinationally for potential branch/comparison extensions.
Purely combinational (`always @(*)`) — fits entirely within the single-cycle datapath with no extra latency.
07
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 10
RTL CODE SPOTLIGHT
control_unit.v — Instruction Decode
Design notes
Pure combinational decoder — one `case` on the 3-bit opcode drives all five control signals plus `alu_op`.
Safe defaults at the top of the always-block mean any unused opcode (5–7) quietly decodes as a harmless NOP.
LOAD asserts `mem_read`, `alu_src` (base+offset addressing) and `mem_to_reg` together — three signals, one decode.
STORE is the only instruction that needs `mem_write` instead of `reg_write`.
08
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 11
TEST PROGRAM
Sample Program Loaded into Instruction ROM
Program walk-through
LOAD R1, 0x10
R1 ← Mem[16] = 5
LOAD R2, 0x11
R2 ← Mem[17] = 10
ADD R3, R1, R2
R3 ← 5 + 10 = 15
STORE R3, 0x12
Mem[18] ← 15
AND R4, R1, R2
R4 ← 5 & 10 = 0
This exact 5-instruction sequence is used to verify both the single-cycle and the pipelined designs, so their results can be compared directly.
09
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 12
VERIFICATION — SINGLE-CYCLE
risc_top.v Wiring & Simulation Pass
Execute → Memory → Write-Back wiring inside risc_top.v
10
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 13
Control Signal Truth Table
10
RISC-V PROCESSOR — INTERNSHIP PROJECT
reg_write→ 1 if the instruction writes a result back to the register file
mem_write → 1 for STORE (writes ALU-computed address/data into data memory)
mem_read→ 1 for LOAD (data memory is combinationally readable in this design)
alu_src → 0 = ALU operand B comes from register file (R-type)
1 = ALU operand B comes from immediate (LOAD/STORE address calculation)
mem_to_reg→ 0= write-back from ALU result
1= write-back from memory (LOAD only)
alu_op → selects ALU operation: - `00` = ADD ,`01` = SUB ,`10` = AND ,`11` = OR ,LOAD/STORE always use ADD (base + immediate)
Opcode | Instr | reg_write | mem_write | mem_read | alu_src | mem_to_reg | alu_op
000 | ADD | 1 | 0 | 0 | 0 | 0 | 00
001 | SUB | 1 | 0 | 0 | 0 | 0 | 01
010 | AND | 1 | 0 | 0 | 0 | 0 | 10
011 | OR | 1 | 0 | 0 | 0 | 0 | 11
100 | LOAD | 1 | 0 | 1 | 1 | 1 | 00
101 | STORE | 0 | 1 | 0 | 1 | 0 | 00

## Slide 14
VERIFICATION — SINGLE-CYCLE
Simulation Waveform (Icarus Verilog)
PASS — PC advances 0→8 across five instructions; each LOAD / ADD / AND drives reg_write with the correct write-back value, and STORE asserts mem_write for exactly one cycle.
11
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 15
GOING FURTHER
From Single-Cycle to a 2-Stage Pipeline
Splitting the datapath into Stage 1 (Fetch + Decode) and Stage 2 (Execute + Memory + Write-Back) lets a second instruction start before the first finishes — but creates a data hazard.
The Hazard
ADD R3,R1,R2 (Stage 1: reading R1,R2)
STORE R3,0x12 (Stage 1, one cycle later)
STORE needs R3 — but ADD's result is still finishing in Stage 2 of the SAME cycle. The register file hasn't been written yet.
The Fix — Forwarding
Since this ISA has no branches, instead of stalling, the write-back value is bypassed directly into Stage 1's register reads the moment it's available — same cycle, no bubble.
risc_top_pipelined.v — forwarding mux logic
12
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 16
VERIFICATION — PIPELINED
Forwarding Resolves Both Hazards
PASS
Write-back now lands one cycle after each instruction enters the pipeline (wb_waddr/wb_wdata trail pc by one step) — yet R3 = 15 and Mem[0x12] = 15 still come out correct, proving the forwarding paths caught both the ADD→STORE and the LOAD→ADD hazards.
13

## Slide 17
IMPLEMENTATION
Synthesis in Vivado — A Key Lesson
risc_top_pipelined_utilization_synth.rpt • Target: xcau7p-fcva289-2-e
Why does it report 0 LUTs?
risc_top / risc_top_pipelined expose only clk and rst — there are no output ports carrying results off-chip. With nothing observable at the boundary, Vivado's synthesis optimizer treats the entire datapath as logic with no effect on any output and trims it away entirely.
Fix: add observable output ports (e.g. expose a register/ALU result, or instantiate inside a wrapper that drives LEDs/registers), then re-run synthesis to see the true LUT/FF/CARRY8 count.
Takeaway
Functional correctness in simulation does not guarantee a meaningful synthesis result — testbench-only designs need real I/O boundaries before utilization numbers mean anything.
14
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 18
REFLECTION
Key Learnings & Challenges
15
RISC-V PROCESSOR — INTERNSHIP PROJECT
Wiring six independently-correct modules together surfaces bugs that unit tests never see — bus-width mismatches and signal-name typos in particular.
Because this ISA has no branches or multi-cycle ops, forwarding alone was enough — a stall/bubble mechanism would only be needed for a longer pipeline.
A self-checking testbench passing in Icarus Verilog says nothing about what survives synthesis optimization — the 0-LUT report was the clearest proof of that.
Pipelining isn't just "split the logic in half" — every shared resource (the register file) becomes a place where timing assumptions can silently break.
Datapath integration
Forwarding vs Stalling
Hazard Awareness
Simulation ≠ synthesis

## Slide 19
Mentor Deliverable Checklist
15
RISC-V PROCESSOR — INTERNSHIP PROJECT
GitHub repository with code, testbench, and README
https://github.com/vaibhavshromani/8_bit_RISC_V
Block diagram: full datapath with all modules and signal connections labeled. Slide 6, 7
Pipeline enhancement (2-stage: Fetch + Execute) — bonus improvement. Slides 15
Optimization report: LUT count, timing analysis .(power & implementation) Slides 12,17
RTL schematic generated from Vivado or Quartus. Slide 8
Final report: design decisions, challenges faced, results, and future scope. Slides 3–18
Control signal truth table: one row per instruction. Slide 13 (ISA table)
Simulation waveforms: PC progression, register updates, memory access. Slide8-11
Testbench: instruction program covering ADD, SUB, AND, OR, LOAD, STORE. Slides 9–12
Verilog source: all component modules + top-level integration file (risc_top.v). Slides 6–11
ISA document: instruction formats, opcode table, register file specification. Slide 5
Execution cycle count per instruction (for performance analysis). Slide 13
✓
✓
✓
✓
✓
✓
✓
✓
✓
✓
✓
✓

## Slide 20
WRAP-UP
Conclusion & Future Scope
Conclusion
Designed a working 8-bit processor from scratch around a custom 16-bit ISA — 6 instructions, 2 instruction formats.
Verified both a single-cycle and a 2-stage pipelined implementation with self-checking Verilog testbenches in Icarus Verilog.
Confirmed data-forwarding correctly resolves RAW hazards introduced by pipelining, with identical final state in both versions.
Carried the design through Vivado synthesis and learned to interpret (and explain) a utilization report.
Future Scope
Add branch / jump instructions, which would require real hazard detection (stalls), not just forwarding.
Extend the pipeline to 5 stages (IF/ID/EX/MEM/WB) for a closer match to classic RISC architectures.
Expose proper top-level I/O so Vivado synthesis reports meaningful LUT / FF / timing numbers.
Target an FPGA board for a live hardware demo of program execution.
16
RISC-V PROCESSOR — INTERNSHIP PROJECT

## Slide 21
Thank You
Vaibhav Shromani
Electronics & Communication Engineering
Maulana Azad National Institute Of Technology, Bhopal
TechnGlobal Industrial Training Program | May-June 2026
VLSI Domain – Major Project
TECHNGLOBAL PRIVATE LIMITED | info@technglobal.in | www.technglobal.in